## Slide 1: Dimensionnement Equillizer
Initial Idea:
FFT Depth at 16384(2^14)
16 bars from 20 to 20kHz
Fs=48kHz
To detect a 20Hz signal, FFT must look for at least 50ms for 1 period. With the above values, the FFT would look over 341ms.
Problem
it generates a frame also every 341 ms, which is 3 FPS, and visually wasn’t good looking.
It also creates an input lag on the display by the same amount of time + the rest of the FPGA delay.
 Was too far behind the sound to make it look good.

## Slide 3
New Stats:
FFT Depth at 8192 (2^13)
22 bars for more granularity
fs=96kHz
A frame is then generated every 85ms, which makes 11 FPS, visually acceptable, same for the input lag.
The low frequencies, difficult to observe, are removed and the 1st bar will take frequencies up to 160Hz.
The number of bars are increased to 22, for more granularity.

## Slide 4
160
200
250
315
400
500
630
800
1k
1.25k
1.6k
2k
2.5k
3.15k
4k
5k
6.3k
8k
10k
12.5k
16k
20k

## Slide 5: Creating the Bars amplifications
Adds up all the amplitudes seen to the specified frequency based on a LUT table
Frequency Hz |  | AXI_user_index
160 |  | 14
200 |  | 17
250 |  | 21
315 |  | 27
400 |  | 34
500 |  | 43
630 |  | 54
800 |  | 68
1000 |  | 85
1250 |  | 107
1600 |  | 137
2000 |  | 171
2500 |  | 213
3150 |  | 269
4000 |  | 341
5000 |  | 427
6300 |  | 538
8000 |  | 683
10000 |  | 853
12500 |  | 1067
16000 |  | 1365
20000 |  | 1707

## Slide 6: Scope visualization
The scope uses 2 block Rams to display the sound wave.
The first block Ram is constanlty updated with sound samples.
The 2nd block ram is there to have coherent information through a single frame when displaying it.